## Slide 1: BITS Pilani Digital Design
Prof. GSS Chalapathi, Prof. Saurabh Gandhi (EEE department)

## Slide 2
Decoders

## Slide 3
Building a decoder

## Slide 4
Building a decoder – the circuit

## Slide 5
Decoders can include an enable input (EN)
EN = 0 disables the decoder (all outputs are 0)
EN = 1 enables the decoder (exactly 1 output is 1 depending on the input)
Decoders with ‘enable’ inputs

## Slide 6
3 – to – 8 decoder

## Slide 7
Building a 3 - to - 8 decoder
Can you think of a ‘hierarchical’ design for this decoder, like we did with half and full adders?

## Slide 8
Hierarchical decoder design
Verify this circuit: use equations for the 2-to-4 decoder to derive equations for 3-to-8 decoder!

## Slide 9
Address decoding
Data routing
7-segment displays
Implementing other digital circuits!
Do the truth table and equations look familiar?
What is a decoder used for?
Decoders are minterm generators!
Used to generate any Boolean expression

## Slide 10
Example: building an adder with decoder(s)
Verify:
Reuse the same decoder for both outputs:
(Dis)advantages of this approach?

## Slide 11
Active-high and active-low decoders

## Slide 12
Active-low decoders are maxterm generators!

## Slide 13
Active-low decoder example

## Slide 14
Opposite function as that of a decoder
Takes 2n inputs, and generates the binary equivalent of the input rank as output
Encoders

## Slide 15
Two ambiguities associated with the design of the simple encoder shown previously:
It assumes only one input to be active. If two inputs are simultaneously active, output becomes invalid.
D0 = 1 or all Ds = 0 will both generate an output of 0
Encoder design issues
Solution: Priority encoders
Multiple asserted inputs allowed; one has priority over others
Separate indication of no-asserted-inputs

## Slide 16
Example: 4-to-2 priority encoder
If two or more inputs are simultaneously 1, output will correspond to the rank of the highest priority input
‘Valid’ output indicator, set to 1 only if at least one of the inputs is 1

## Slide 17
Use of binary encoder (example)

## Slide 18
Uses of priority encoders (example)