## Slide 1: BITS Pilani Digital Design
Prof. GSS Chalapathi, Prof. Saurabh Gandhi (EEE department)

## Slide 2
Multiplexers – digital traffic lights

## Slide 3
2–to–1 multiplexer

## Slide 4
Building a multiplexer

## Slide 5
Building a multiplexer – the circuit

## Slide 6
Multiplexers with Enable input

## Slide 7
Truth table abbreviations

## Slide 8
More abbreviations

## Slide 9
4–to–1 mux
Block diagram and truth table
What is that bubble at the input of EN?
This is an active-low enable input multiplexer, i.e. when EN pin is made 0, output will select some input; when EN pin is 1, the multiplexer outputs 0
Useful for hierarchical designs (we will see later)!

## Slide 10
4-to-1 mux implementation

## Slide 11
2n-to-1 multiplexers

## Slide 12
n variable functions use an n-input multiplexer (n-to-1)
The n variables connect to the select input pins of the mux, thereby selecting on row of the truth table
data inputs are chosen intelligently to get the correct output
For each minterm to be included in the SOP, we connect the corresponding data input of the mux to 1; rest to 0
Implementing Boolean functions with muxes – addition

## Slide 13
An adder with a smaller mux

## Slide 14
An adder with a smaller mux

## Slide 15
Adder with smaller mux – implement the sum

## Slide 16
Dual 4-to-1 mux: Instead of selecting 1 out of 4 input bits, selects 1 2-bit input out of 4 2-bit inputs
Dual multiplexers

## Slide 17
Building dual multiplexers

## Slide 18
Adder with dual mux – combining sum and carry in a single device

## Slide 19
Implement the Boolean function F(A,B,C,D) = Σ (0,1,3,4,8,9,15)
Example

## Slide 20
Transmit information from a single line on to one of 2n lines
Selection of output line determined by n select lines
A decoder with enable input can function as a demux
De-multiplexers